## Slide 1: Smart Manufacturing Pilot Use Case 2: Threat Detection & Isolation
Notes: UC1: saw how easy it is to setup new manufacturing machines, connect them, collect their data – thanks to 5GTANGO’s SP and our developed flexible NSs + FMP
 UC2: Threat Detection & isolation  next slide

## Slide 2: Use Case 2: Threat Detection & Isolation
Situation: Machines running & collecting data
Goals of use case 2:
  Monitor machines in production
  Automatically detect problems  Here: Detect intrusion
  Automatically resolve problems  Here: Isolate intruded machine
Challenges:
  Real-time monitoring & IDS
  Flexible reconfiguration of services and CNFs
  Automation
Notes: Machines are running & data being collected  make sure it stays that way (stable)
Ex: Attacker wants to intrude (access/modify data)

## Slide 3: High-Level Architecture: Normal Production
Intrusion!
Notes: Normal production: Machine  NS2  NS1  Cloud
Intrusion: Ensure no malicious data is sent to NS1 and cloud
But also don’t throw data away  analyze, debug, maybe merge later

## Slide 4: High-Level Architecture: Intrusion
Intrusion!
Notes: What we did:
IDS in each NS2 to detect if someone unauthorized tries to connect
Quarantine NS1 (shadow copy)
 data isolated  threat contained  data still available for analysis

## Slide 5: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
MDC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: Realize flexible, automated detection & reconfig via 5GTANGO SP  multiple advanced components play together
Start: NS2 (IDS, MDC)  NS1
Powerful  could also be used for more complex attacks/actions based on monitoring data

## Slide 6: Demo Steps
Starting point:
  Normal & Quarantine NS1 running
  NS2 running and machine connected, sending data
Intrusion attempt by outside attacker
IDS notices intrusion and triggers alert
NS2 is reconfigured to send data into quarantine NS1
 Threat detected & isolated!

## Slide 7: Starting point: Machines in Production
Notes: EAE
normal: data arrives in normal NS1 (left)
not quarantine (right)

## Slide 8: Intrusion Attempt by Attacker
Notes: attacker already in factory network and IP of NS2
open ports  Samba  connect

## Slide 9: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
MDC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: intrusion  detected by IDS

## Slide 10: Intrusion Detection by IDS

## Slide 11: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
MDC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: IDS sets alarm metric
alert triggered in monitoring system

## Slide 12: Intrusion Alert

## Slide 13: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
MDC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: reconfig through SP
then send data to quarantine

## Slide 14: Isolation of Intruded Machine

## Slide 15: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
MDC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Threat detected & contained!
Notes:  threat detected & contained  success

## Slide 16: Thanks!