## Slide 1: Smart Manufacturing Pilot Use Case 2: Threat Detection & Isolation

## Slide 2: Use Case 2: Threat Detection & Isolation
Situation: Machines running & collecting data
Goals of use case 2:
  Monitor machines in production
  Automatically detect problems  Here: Detect intrusion
  Automatically resolve problems  Here: Isolate intruded machine
Challenges:
  Real-time monitoring
  Cloud-native intrusion detection system (IDS)
  Flexible reconfiguration of services and CNFs
  Automation of threat detection & isolation
Notes: UC1: saw how easy it is to setup new manufacturing machines, connect them, collect their data
UC2: Machines are running & data being collected  make sure it stays that way (stable)
Ex: Attacker wants to intrude (access/modify data)

## Slide 3: High-Level Architecture
Intrusion!
New in use case 2:
  Intrusion Detection System (IDS)
  Quarantine NS1
Normal production:
  Data arrives in production NS1
Notes: Normal production: Machine  NS2  NS1  Cloud
Intrusion: Ensure no malicious data is sent to NS1 and cloud
But also don’t throw data away  analyze, debug, maybe merge later  Quarantine NS1

## Slide 4: High-Level Architecture
Intrusion!
New in use case 2:
  Intrusion Detection System (IDS)
  Quarantine NS1
Normal production:
  Data arrives in production NS1
Intrusion:
  Intrusion detected by IDS
  NS2 reconfigured
  Data arrives in quarantine NS1
 Threat detected & contained
Notes:  data isolated  threat contained  data still available for analysis

## Slide 5: Details: Intrusion Detection & Reconfiguration
NS1 (Quarantine)
NS1 (Quarantine)
NS1 (Production)
IDS
(Suricata + ELK)
Machine Data
Collector (MDC)
Function Lifecycle Manager
Service Lifecycle Manager
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
NS1 (Production)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: Realize flexible, automated detection & reconfig via 5GTANGO SP  multiple advanced components play together
Innovative features: Programmability & flexibility of FSM/SSM, Run-time actions via policies
Powerful  could also be used for more complex attacks/actions based on monitoring data

## Slide 6: Demo Steps
Starting point:
  Normal & Quarantine NS1 running
  NS2 running and machine connected, sending data
Intrusion attempt by attacker
IDS notices intrusion and triggers alert
NS2 is reconfigured to send data into quarantine NS1
 Threat detected & isolated!

## Slide 7: Starting point: Machines in Production
Normal NS1
Quarantine NS1
Notes: normal: data arrives in normal NS1 (left)
not quarantine (right)

## Slide 8: Intrusion Attempt by Attacker
Notes: attacker already in factory network and IP of NS2
open ports  Samba  connect

## Slide 9: Details: Intrusion Detection & Reconfiguration
NS1 (Quarantine)
NS1 (Production)
IDS
(Suricata + ELK)
Machine Data
Collector (MDC)
Function Lifecycle Manager
Service Lifecycle Manager
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
NS1 (Production)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: intrusion  detected by IDS

## Slide 10: Intrusion Detection by IDS
Notes: dashboard shows intrusions
IDS shows intrusion characteristics
eg, username of intruder

## Slide 11: Details: Intrusion Detection & Reconfiguration
NS1 (Quarantine)
NS1 (Production)
IDS
(Suricata + ELK)
Machine Data
Collector (MDC)
Function Lifecycle Manager
Service Lifecycle Manager
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
NS1 (Production)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: IDS sets alarm metric
alert triggered in monitoring system

## Slide 12: Intrusion Alert
Notes: monitoring rule through policy
green  red = intrusion alarm, trigger reconifg

## Slide 13: Details: Intrusion Detection & Reconfiguration
NS1 (Quarantine)
NS1 (Quarantine)
NS1 (Production)
IDS
(Suricata + ELK)
Machine Data
Collector (MDC)
Function Lifecycle Manager
Service Lifecycle Manager
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: reconfig through SP
then send data to quarantine

## Slide 14: Isolation of Intruded Machine
Threat detected & contained!
Notes: data stops arriving in normal NS1
starts arriving in quarantine NS1
 isolated  success

## Slide 15: Alternative: Manual Isolation
Factory staff notices anomaly  Trigger isolation through FMP
Later: Deisolation
Function Lifecycle Manager
Service Lifecycle Manager
FMP
SMP-CC
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
Staff
Manual
Trigger
Reconf. Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconf.

## Slide 16: Alternative: Manual (De-)Isolation

## Slide 17: Use Case 2: Conclusions
Real-time monitoring of production machines
Automatic intrusion detection
Automatic reconfiguration and machine isolation
Alternative: Manual isolation & deisolation
Enabled by 5GTANGO service platform advanced features

## Slide 18: Thanks!

## Slide 19: Details: Intrusion Detection & Reconfiguration
IDS
(Suricata + ELK)
Machine Data
Collector
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
to NS1 (Production)
to NS1 (Quarantine)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
Reconf.
Result
(MDC)
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: Realize flexible, automated detection & reconfig via 5GTANGO SP  multiple advanced components play together
Start: NS2 (IDS, MDC)  NS1
Powerful  could also be used for more complex attacks/actions based on monitoring data

## Slide 20: Details: Intrusion Detection & Reconfiguration
NS1 (Quarantine)
NS1 (Quarantine)
NS1 (Production)
IDS
(Suricata + ELK)
Machine Data
Collector (MDC)
Function Lifecycle Manager
Service Lifecycle Manager
Func.-Spec. Manager (MDC)
Service-Spec. Manager
(NS2)
Policy Manager
Monitoring Manager
5GTANGO Service Platform
NS2: Machine Interconnection
NS1 (Production)
Machine Data
IDS Alarm Metric
Alarm Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconfigure MDC CNF
Intrusion!
Notes: Realize flexible, automated detection & reconfig via 5GTANGO SP  multiple advanced components play together
Innovative features: Programmability & flexibility of FSM/SSM, Run-time actions via policies
Powerful  could also be used for more complex attacks/actions based on monitoring data

## Slide 21: Alternative: Manual Isolation
Factory staff notices anomaly  Trigger isolation through FMP
Later: Deisolation
FMP
SMP-CC
FSM (MDC)
SSM (NS2)
FLM
SLM
Policy Manager
Monitoring Manager
5GTANGO Service Platform
Staff
Manual
Trigger
Reconf.
Trigger
Reconf. Trigger
Reconf.
Trigger
Reconf.
Trigger
Reconf.
Event
(MDC)
Reconf.
Event
Reconf.
Task
(MDC)
Reconf.

## Slide 22: Credits
Checkmark icon by Icons8